## Slide 1: OpenXAL status at ESS
Juan, Emanuele, Natalia, Yngve, Sofia
www.europeanspallationsource.se
21 November, 2017

## Slide 2: Framework
ESS OpenXAL version now 1.1.0 (and 1.1.1-SNAPSHOT)
Build & test system has been upgraded, using Jenkins pipelines now.
Deployment strategy changed, will make one big tarball for deployment (rather than a shell script which runs many commands)
LEBT section added to the ESS model

## Slide 3: Update on ESS Model (JELS)
JELS was doing calculations in the beam frame of reference instead of the lab frame (Open XAL default)
All transfer maps were updated to use the lab frame and be consistent with Open XAL convention (including space-charge)
RF Fieldmap – integrator optimized and corrected for LIVE simulations (broken)
New elements:
  ESS DTLTank class, using our RFGap implementation
  Solenoid fieldmap for the LEBT
All unit tests redone and benchmarked against TraceWin

## Slide 4: Applications update
Removed Modelmanager, will reuse parts of the logic in other applications
Application in beta, Trajectory Correction (replacing Orbit Correction)
Application in alpha, LEBT Application
Application in alpha version, Scanner (replacing Scan1D, Scan2D)
Application in development, Configurator (replacing some logic in MM, optics switcher, tracewin importer and more)

## Slide 5: Trajectory Correction
JavaFX
One-to-one works
SVD correction also working
Ability to define any set of BPM+steerers for correction (no sequence boundaries)
Support Applications: Trajectory Display (displays the bare trajectory and/or trajectory difference to a reference)

## Slide 6: LEBT Application
JavaFX
Solenoid field as maps
Corrector superimposed to solenoids
Center of mass and envelope calculations
Some PVs from the ion source implemented
Idea: quick modeling and display of the LEBT main features and diagnostics. Supposed to aid during commissioning.

## Slide 7: Scanner
JavaFX
Scan N variables, read M variables (plus the scan ones)
Can limit scan by functions
Select a PV from multiple elements at once (e.g. xAvg from all BPM)
Borrowed code from Model Browser
Basic plotting, no analysis

## Slide 8: Configurator
JavaFX
Import from TraceWin (formerly in model manager), both from files or git repository
Replace Optics Switcher
RBAC enable switch

## Slide 9: Discussion Topics
Java9?
IPAC and other conferences next year?